## Slide 1: PORTION OF FLORENCE WILLIAMSBURG COMMON BOUNDARY RE-ESTABLISHMENT PRESENTATION October 24, 2016 Lake City, South Carolina

## Slide 2: SC Code of Law and Act 262 Of 2014
Role of South Carolina Geodetic Survey
      (1994) Dispute between two or more counties- SCGS will act as mediator to resolve the dispute
      (1994/2014) SCGS to assist counties in defining and monumenting the locations of county boundaries and positioning the monuments using geodetic surveys where counties are ill-defined, unmarked, or poorly marked
      (2014) SCGS will clarify county boundaries as defined in Chapter 3, Title 4
      (2014) SCGS will analyze archival and other evidence and perform field surveys to position geographically all county boundaries in accordance with statutory descriptions

## Slide 3
Notify County Administrators in advance of planned work
Conduct historical research for documentary evidence of boundaries
Perform field work to locate monuments and corroborating evidence and position on State Plane Coordinates
Share preliminary findings with county officials for impact analysis and to plan public meetings
Receive feedback and input from local officials and public
Review and update findings, as appropriate
Work to build cooperation with affected parties
Steps for Clarifying Boundaries

## Slide 4: Public Meeting Notification

## Slide 5: THE FLORENCE COUNTY ANNEXATION – WILLIAMSBURG COUNTY
FLORENCE COUNTY WAS CREATED ON DECEMBER 22, 1888.
ITS PARENT COUNTIES COMPRISED OF DARLINGTON, MARION, WILLIAMSBURG, AND CLARENDON COUNTIES. AFTER FLORENCE COUNTY WAS CREATED, IT HAS UNDERGONE FOUR ANNEXATIONS.
THIS EXHIBIT IS TO PROPERLY RETRACE THE FOURTH AND FINAL ANNEXATION ALONG THE SOUTHERN ROUTE OF THE ANNEXATION. THE PETITION FOR THE FOURTH ANNEXATION OCCURRED ON MARCH 4, 1921 AND COMPRISED 45.3 SQUARE MILES.

## Slide 6
SUBJECT PORTION OF THE COMMON BOUNDARY LINE

## Slide 7: THE FLORENCE COUNTY ANNEXATION- WILLIAMSBURG COUNTY
This is a list of the items used to prepare this current plat:
Field survey data; using modern surveying practices
Physical evidence on or near the subject county line
Reference material
  South Carolina Code of Laws
  S. C. Archive Documents
  Plats of Record
  SCDOT Highway Plans
  USGS Quadrangle Maps
  Soil Survey of Williamsburg County, SC

## Slide 8: THE FLORENCE COUNTY ANNEXATION- WILLIAMSBURG COUNTY

## Slide 9: The South Carolina Code of Laws-Florence County

## Slide 10: The South Carolina Code of Laws-Williamsburg County

## Slide 11: PETITION FOR ANNEXATION OF A PORTION OF FLORENCE COUNTY TO WILLIAMSBURG COUNTY
Unsuccessful
Petition

## Slide 12
The April 18th, 1920 Coggeshall-Wilson Boundary Plat
References

## Slide 13: 1920’s Surveyors
Reference

## Slide 14
1920’s Surveying Instruments and Practice

## Slide 15: Map of Survey

## Slide 16: Lynches Creek along Old Georgetown Road to the Road Intersection with Vox Highway
Section 1

## Slide 17: Point of Beginning
Lynches Creek

## Slide 18: Coggeshall-Wilson Plat 1944 Aerial Photo
Aerial References:
UNIVERSITY OF SOUTH CAROLINA
THOMAS COOPER LIBRARY
SOUTH CAROLINA FORESTRY COMMISSION

## Slide 19: Coggeshall-Wilson Plat 1928 Williamsburg County Soil Map
References:
Soil Survey of Williamsburg County, SC
By W.J. Latimer, B.H. Hendrickson, F.R., Lesh, A.H Hasty, W.E. Tharp, and C.S. Simmons
UNIVERSITY OF SOUTH CAROLINA
USDA Historical Soil Survey Maps of SC Digital Collection

## Slide 20: Lynches Creek and Old Georgetown Road
County Line
Old Georgetown Road
S 21-58
Probable Run of Lynches Creek

## Slide 21: Lynches Creek and Old Georgetown Road-Aerial
Bridge
Bridge
Bridge
Bridge
POB Coggshall-Wilson Plat
GIS Mapping

## Slide 22: Map of Survey
Soils Map

## Slide 23: SCDOT Plans-Florence County Old Georgetown Road S 21-58
Resurvey 2015 indicates County Line being at this run
Dashed line indicates dirt road of 1971 was not outside of SCDOT R/W
GIS Line Location

## Slide 24: SCDOT Plans-Florence County Old Georgetown Road S 21-58

## Slide 25: County Line along the Old Georgetown Road
The field evidence supports that the current road appears to be in the same location as the Coggeshall-Wilson plat. No evidence of old roadbed.
North View
South View
South View

## Slide 26: SCDOT Plans-Aerial Comparison
1944 SCDOT Plans 2013

## Slide 27: Aerial \ Soil –Coggeshall-Wilson Plat Comparison
1944 1928

## Slide 28: Aerial –Coggeshall-Wilson Plat Comparison
USDA 2011

## Slide 29: Road Intersection with Vox Highway to current Cowhead Road
Section 2

## Slide 30: Point of Beginning Section 2
1944
2013

## Slide 31: Coggeshall-Wilson Plat – 1944 Aerial
1944
Coggeshall-Wilson Plat

## Slide 32: Coggeshall-Wilson Plat – 1928 Soil
1928
Coggeshall-Wilson Plat

## Slide 33: Old Farm Road
Old Farm Road

## Slide 34: Quail Road (Florence)-Williamson Road (Williamsburg)
S 21-633
S 45-496
Pavement Edge

## Slide 35: Arrowhead Road (Florence)
South View

## Slide 36: Blackberry Road (Williamsburg)

## Slide 37: Whispering Pines Road at Altman Road (Williamsburg)
Altman Road

## Slide 38: St . James Road ( Florence-Williamsburg)
St. James Road

## Slide 39: Intersection County Road s 45-84 with Cowhead( Florence) Cow Head (Williamsburg)

## Slide 40: Intersection County Road s 45-84 with Cowhead( Florence) Cow Head (Williamsburg)

## Slide 41: Intersection County Road S 45-84 with Cowhead( Florence) Cow Head (Williamsburg)

## Slide 42: Coggeshall-Wilson Plat
1944 Aerial Photos

## Slide 43: Coggeshall-Wilson- 2015 Map of Survey
Coggeshall-Wilson Plat
2015 Resurvey Plat

## Slide 44
Detail of the western end point of county boundary shown on Coggeshall-Wilson plat as S72 20E 43,610’. Resurvey of this line indicates bearing of S74 42 24E and 43,569.68’ distance.
Difference in direction can be attributed to several variables such as method of collection i.e. magnetic compass as opposed to GNSS , NAD 83 (2011) datum Local attraction or instrumental errors or errors in observation in magnetic compass.
See above cited reference of 1920’s survey that may point to less accurate methods that give possible explanation for differences in distance between the 1920 survey and the 2015 resurvey distance.

## Slide 45: Coggeshall-Wilson Plat
1944 Aerial Photo

## Slide 46: Coggeshall-Wilson Plat
1928 Soil Map

## Slide 47
These three corners were established by overlaying alignment of the highway plans for W. County road (S 21-40) and Midway road (S 21-111 and S 45-84) onto current field survey data. (1008) is at the intersection of the alignment of highway plans for W. County road (S 21-40), and Midway road (S 21-111). (1007) is along the highway plans alignment for the referenced distance of 316' to (1007) and then turning along the highway alignment of Midway road (S 45-84) for the reference distance of 726' to (1006) as shown on the referenced Coggeshall-Wilson plat.

## Slide 48
The Coggeshall-Wilson plat clearly shows a distance of 726 ‘ and 316' for describing the line length along S 21-84/S-21-111 (Midway road).
The 726’ distance is omitted from the Statue Description.

## Slide 49: Plat Magnification
Additionally, the 726’ appears to be mislabeled as “N 26° E” in the Statue Description.
Scrivener's Error

## Slide 50: SCDOT Plans- Highlighted comparison
Midway Road
Represents Depicted County Line
Represents Indiantown\Midway Road
Represents Cowhead Road
Rotated View
Coggeshall-Wilson Plat

## Slide 51: Road Intersection Cowhead Road along W. County Road (formally Kingstree Road) to Flannigan’s Creek
Section 3

## Slide 52: Point of Beginning Section 3

## Slide 53: County Road S 45-84 (Williamsburg)
W. County Line Road

## Slide 54
The reference material indicates from the county boundary corner (1008) along W. County road (formally Kingstree road according to the Coggeshall-Wilson plat) is bearing N 71°35' E, 10,094'. However, by using the highway plans for this road (S 21-40) and the field survey data, the Coggeshall-Wilson plat distance appears to be in error. It is our determination that the distance is 7,094.00' instead of 10,094.00' for this line.
This conclusion is based on observed evidence of the location of the current road and by the study of highway plans and historical aerial photography and lack of evidence in the field to show the road extended to a distance of 10,094’.

## Slide 55: County Road S 45-40 and S 45-430 (Williamsburg)
W. County Line Road

## Slide 56
Beginning at Midway road and bearing N 68°46‘30" E along W. County road, 7,094.00' is near the start of a curve of the current road. The highway plans for W. County road (S 21-40) show an old road at or near this point (1009) that turns to an easterly direction. The Coggeshall-Wilson plat and the referenced code of laws state the county boundary in an easterly direction for 504.00' with road, and then turns southeasterly with the road for 527'. This old road eventually ties back into the current road as indicated on the highway plans (S 21-40).

## Slide 57: 2015 Map of Survey
As the county boundary reconvenes with road alignment of W. County line road (S 45-40) at corner (1011), it continues with the road alignment to the intersection of W. County line and Wall road. By employing the highway plans for the road and by field survey data, county line corner (1012) was determined.
From point (1012) the county line runs with the road alignment (corners 1012 through 1016) to point (1017). The county line east of point (1017), leaves the road alignment as indicated on highway plans S 21-40, docket 45.332 pt.2, sheet 11. During our field survey, a discernible road bed was determined and data collected for the old roadbed. Corners (1018), (1019), (1020), and (1021) are along old roadbed.

## Slide 58
As the county boundary reconvenes with road alignment of W. County line road (S 21-40) at corner (1011), it continues with the road alignment to the intersection of W. County line and Wall road. By employing the highway plans for the road and by field survey data, county line corner (1012) was determined.
From point (1012) the county line runs with the road alignment (corners 1012 through 1016) to point (1017). The county line east of point (1017), leaves the road alignment as indicated on highway plans S 21-40, docket 45.332 pt.2, sheet 11. During our field survey, a discernible road bed was determined and data collected for the old roadbed. Corners (1018), (1019), (1020), and (1021) are along old roadbed.

## Slide 59: County Road S 45-40 (Williamsburg)
W. County Line Road

## Slide 61: County Road S 45-40 (Williamsburg)
W. County Line Road

## Slide 62: County Road S 45-40 (Williamsburg)
W. County Line Road

## Slide 63: County Road S 45-40 (Williamsburg)
W. County Line Road

## Slide 64: Intersection of County Road S 45-40 (Williamsburg) and SC Highway 41/51
W. County Line Road
SC Hwy 51

## Slide 65: County Road S 45-40 (Williamsburg) at Flanagan’s Creek

## Slide 66
FLORENCE AND WILLIAMSBURG COMMON BOUNDARY

## Slide 67: Act 262 of 2014
SCGS Requirements:
    Upon reestablishing county boundary, SCGS shall certify its work and within 30 days of certification:
        Provide copies to the administrator of each affected county;
        Provide written notification to affected parties
        Provide notice and copies to the public through its official website and or other means it considers appropriate; and
        Notify as it determines appropriate, other affected state and federal agencies
    (Initiates 60 Day Appeal Process)
  Certified Surveys submitted to Secretary of State, Register of Deeds Offices, and South Carolina Department of Archives with Cover Letter
  Date of the cover letter is the date the surveys become effective
  Introduce Legislation to update Code of Law to reflect clarified boundary with State Plane Coordinates
Steps for Clarifying Boundaries

## Slide 68: Act 262 of 2014
Affected Parties Disagreeing with SCGS:
    May file request for a contested case hearing with the SC Administrative Law Court
    This decision may be appealed
    “Affected Party”
              Governing body of an affected county
              Governing body of a political subdivision of this State
              An elected official, other than a statewide elected official
              A property owner or an individual residing in the certification zone
              A business entity located in the certification zone
              A nonresident individual who owns or leases real property situated in the certification zone

## Slide 69: SIGNIFICANT IMPACTS?
A significant impact is defined as a residence or place of business being found in a different county based on the re-established boundary.
Reviewed Over 150 Properties Along the 12.5 Mile Section of Re-established Boundary:
Determined 5 Significant Impacts
With 4 being found in Florence
And 1 being found in Williamsburg

## Slide 70: QUESTIONS?